## Slide 1: STM32
Snippets

## Slide 2: CONTENT
GPIO lab
EXTI lab
SLEEP lab
STOP lab
STANDBY lab
TIMER lab
ADC lab
UART lab

## Slide 3: Generic setup
All examples will have the system clock configured as below:
The hardware used for all codes is the STM32F072xB device, the same one in the Discovery kit provided

## Slide 4: GPIO Lab 1

## Slide 5: Configure GPIO for LED toggling
Objective
  Learn how to setup pin and GPIO port using Snippets
  How to generate open the example and understand it
Goal
  Configure GPIOA pin0 as input
  Configure GPIOC pin8 as output
  Use a simple template from Snippet
1

## Slide 6: Configure GPIO for LED toggling
Now we open the project in our IDE
  Check the configuration clock for 48MHz
  Configure the GPIO Pins
For toggling we used a simple logic:
1
while (1) /* Infinite loop */
{
if((GPIOA->IDR&0x01))
{
GPIOC->BSRR = (1<<8); //turn on orange led on PC8 when pressed
}
else
{
GPIOC->BRR = (1<<8); //turn off orange led on PC8 when released
}
}
ConfigureGPIO();
SysTick_Config(48000); /* 1ms config */

## Slide 7: EXTI lab 2

## Slide 8: Configure EXTI which turns on LED
Objective
  Learn how to setup input pin with EXTI in Snippets
Goal
  Configure GPIO and EXTI pin
  Check the interrupt vector handler
  Verify the correct functionality by pressing button which turns on LED
  GPIOA pin 0 is the EXTI pin
  GPIOC pin 9 is the LED used
2

## Slide 9: Configure EXTI which turns on LED
Simple code for main function and there is no loop
  Configure the GPIO
  Configure the EXTI
2
ConfigureGPIO();
ConfigureExternalIT();
while (1) /* Infinite loop */
{
}

## Slide 10: Configure EXTI which turns on LED
Configure the GPIO
2
__INLINE void ConfigureGPIO(void)
{
/* (1) Enable the peripheral clock of GPIOC */
/* (2) Select output mode (01) on GPIOC pin 9 */
RCC->AHBENR |= RCC_AHBENR_GPIOCEN; /* (1) */
GPIOC->MODER = (GPIOC->MODER & ~(GPIO_MODER_MODER9)) \
| (GPIO_MODER_MODER9_0); /* (2) */
}

## Slide 11: Configure EXTI which turns on LED
Configure the EXTI
2
__INLINE void ConfigureExternalIT(void)
{
/* (1) Enable the peripheral clock of GPIOA */
/* (3) Configure the corresponding mask bit in the EXTI_IMR register */
/* (4) Configure the Trigger Selection bits of the Interrupt line on rising edge*/
/* (5) Configure the Trigger Selection bits of the Interrupt line on falling edge*/
RCC->AHBENR |= RCC_AHBENR_GPIOAEN; /* (1) */
EXTI->IMR = 0x0001; /* (3) */
EXTI->RTSR = 0x0001; /* (4) */
EXTI->FTSR = 0x0001; /* (5) */
/* Configure NVIC for External Interrupt */
/* (6) Enable Interrupt on EXTI0_1 */
/* (7) Set priority for EXTI0_1 */
NVIC_EnableIRQ(EXTI0_1_IRQn); /* (6) */
NVIC_SetPriority(EXTI0_1_IRQn,0); /* (7) */
}

## Slide 12: Configure EXTI which turns on LED
Interrupt Handler
2
void EXTI0_1_IRQHandler(void)
{
if ((EXTI->PR & 0x0001) != 0) /* Check line 0 has triggered the IT */
{
EXTI->PR |= 0x0001; /* Clear the pending bit */
GPIOC->ODR ^= (1<<9); /* Toggle green led on PC9 */
}
}

## Slide 13: Low Power mode SLEEP lab 3

## Slide 14: SLEEP Mode
DMA
Core
CM4
Power regulator
RAM
Clock
USART
GP timers
DAC
USB
SPI
ADC
I2C
GPIO’s
RTC/backup reg.
IWDG
Reset
Core is stopped
Peripherals are running
Consuption: 164uA@48MHz 84uA@8MHz
HSE
HSI
LSE
LSI
FLASH

## Slide 15: Use SLEEP mode with EXTI
Quick setup for the IDE to enable debug in low power mode
3
To be able reprogram the STM32 which is in LP mode we must use connection under reset option

## Slide 16: Use SLEEP mode with EXTI
Simple main function to configure the EXTI and LED
3
ConfigureGPIO();
ConfigureExternalIT();
while (1) /* Infinite loop */
{
GPIOC->BRR = (1<<8); //turn off orange led on PC8 when released
PWR_EnterSLEEPMode();
while((GPIOA->IDR&0x01))
{
GPIOC->BSRR = (1<<8); //turn on orange led on PC8 when pressed
}
}

## Slide 17: Use SLEEP mode with EXTI
The functions for GPIO and EXTI are the same from the previous exercices
  __INLINE void ConfigureGPIO(void)
  __INLINE void ConfigureExternalIT(void)
  void EXTI0_1_IRQHandler(void)
New function to enable entering in sleep mode
3
__INLINE void PWR_EnterSLEEPMode(void)
{
/* Clear SLEEPDEEP bit of Cortex System Control Register */
SCB->SCR &= (uint32_t)~((uint32_t)1<<2);
/* Select SLEEP mode entry -------------------------------------*/
/* Request Wait For Interrupt */
__WFI();
}

## Slide 18: Low Power mode STOP lab 4

## Slide 19: STOP Mode
Clock
DMA
Core
CM4
Power regulator
FLASH
RAM
USART
GP timers
DAC
USB
SPI
ADC
I2C
GPIO’s
RTC/backup reg.
IWDG
Reset
HSE
HSI
LSE
LSI
Core is stopped
HSE, MSI clocks are OFF
SRAM and registers content is preserved
Peripherals with HSI, LSI, LSE clock option can be ON
GPIO’s keep their setup
Consuption: 7uA
Notes: The Stop mode is based on the Cortex™-M0+ deepsleep mode combined with peripheral clock gating.
HSI ON/OFF is optional

## Slide 20: Use STOP mode with EXTI
Simple main function to enter STOP mode, same logic as Sleep Mode
4
ConfigureGPIO();
ConfigureExternalIT();
while (1) /* Infinite loop */
{
GPIOC->BRR = (1<<8); //turn off orange led on PC8 when released
PWR_EnterSTOPMode();
while((GPIOA->IDR&0x01))
{
GPIOC->BSRR = (1<<8); //turn on orange led on PC8 when pressed
}
}

## Slide 21: Use STOP mode with EXTI
Our different function
4
__INLINE void PWR_EnterSTOPMode(void)
{
uint32_t tmpreg = 0;
/* Select the regulator state in STOP mode ---------------------------------*/
tmpreg = PWR->CR;
/* Clear PDDS and LPDS bits */
tmpreg &= (uint32_t)~(0x00000002U | 0x00000001U);
/* Store the new value */
PWR->CR = tmpreg;
/* Set SLEEPDEEP bit of Cortex System Control Register */
SCB->SCR |= (1UL<<2);
/* Request Wait For Interrupt */
__WFI();
/* Reset SLEEPDEEP bit of Cortex System Control Register */
SCB->SCR &= (uint32_t)~((uint32_t)(1UL<<2));
}
Notes: In run approx. 53mA
Consumption on STM32F429disco approx. 5mA in stop(not optimized)
You ma test the difference with pins ins floating in and analog

## Slide 22: Low Power mode STANDBY lab 5

## Slide 23: STANDBY Mode
Clock
DMA
Core
CM4
Power regulator
FLASH
RAM
USART
GP timers
DAC
USB
SPI
ADC
I2C
GPIO’s
RTC/backup reg.
IWDG
Reset
HSE
HSI
LSE
LSI
Core and all peripherals are OFF, except RTC and IWDG if enabled
HSE, MSI, HSI clocks are OFF, LSI LSE can be ON
SRAM and registers content is lost, except RTC, and standby circuitry
GPIO’s are in high Z, except Reset, RTC OUT and WKUP 1,2,3
Consuption: 2uA
Reset
RTC OUT
WKUP 1,2,3
Notes: The Standby mode allows to achieve the lowest power consumption. It is based on the
Cortex™-M0+ deepsleep mode, with the voltage regulator disabled. The VCORE domain is
consequently powered off. The PLL, the MSI, the HSI16 oscillator and the HSE oscillator
are also switched off. SRAM and register contents are lost except for the RTC registers,
RTC backup registers and Standby circuitry

## Slide 24: Use STANDBY mode with WKPIN
Simple main function to enter STANDBYmode, same logic as Sleep Mode but it’s mandatory to specify the waking up pin (PA0)
5
ConfigureGPIO();
ConfigureExternalIT();
/*Enables the WakeUp PINx functionality, based in the PWM->CSR EWUP1 .*/
PWR->CSR |= (0x00000100U << (uint8_t)1);
while (1) /* Infinite loop */
{
GPIOC->BRR = (1<<8); //turn off orange led on PC8 when released
PWR_EnterSTANDBYMode ();
while((GPIOA->IDR&0x01))
{
GPIOC->BSRR = (1<<8); //turn on orange led on PC8 when pressed
}
}

## Slide 25: Use STANDBY mode with WKPIN
Our different function
5
__INLINE void PWR_EnterSTANDBYMode(void)
{
/* Select STANDBY mode */
PWR->CR |= (uint32_t)0x00000002U;
/* Set SLEEPDEEP bit of Cortex System Control Register */
SCB->SCR |= (1UL << 2);
/* Request Wait For Interrupt */
__WFI();
}
Notes: In run approx. 53mA
Consumption on STM32F429disco approx. 5mA in stop(not optimized)
You ma test the difference with pins ins floating in and analog

## Slide 26: TIMER lab 6

## Slide 27: Configure TIMER which turns on LED
Objective
  Learn how to setup the timer as time base
Goal
  GPIOC pin 9 is the LED used
  TIM15 configured as TimeBase Interrupt
6

## Slide 28: Configure TIMER which turns on LED
Simple code for main function and there is no loop
  Configure the GPIO
  Configure the EXTI
6
ConfigureGPIO();
ConfigureExternalIT();
while (1) /* Infinite loop */
{
}

## Slide 29: Configure TIMER which turns on LED
Configure the GPIO
6
__INLINE void ConfigureGPIO(void)
{
/* (1) Enable the peripheral clock of GPIOC */
/* (2) Select output mode (01) on GPIOC pin 9 */
RCC->AHBENR |= RCC_AHBENR_GPIOCEN; /* (1) */
GPIOC->MODER = (GPIOC->MODER & ~(GPIO_MODER_MODER9)) \
| (GPIO_MODER_MODER9_0); /* (2) */
}

## Slide 30: Configure TIMER which turns on LED
Configure the EXTI
6
__INLINE void ConfigureExternalIT(void)
{
/* (1) Enable the peripheral clock of GPIOA */
/* (3) Configure the corresponding mask bit in the EXTI_IMR register */
/* (4) Configure the Trigger Selection bits of the Interrupt line on rising edge*/
/* (5) Configure the Trigger Selection bits of the Interrupt line on falling edge*/
RCC->AHBENR |= RCC_AHBENR_GPIOAEN; /* (1) */
EXTI->IMR = 0x0001; /* (3) */
EXTI->RTSR = 0x0001; /* (4) */
EXTI->FTSR = 0x0001; /* (5) */
/* Configure NVIC for External Interrupt */
/* (6) Enable Interrupt on EXTI0_1 */
/* (7) Set priority for EXTI0_1 */
NVIC_EnableIRQ(EXTI0_1_IRQn); /* (6) */
NVIC_SetPriority(EXTI0_1_IRQn,0); /* (7) */
}

## Slide 31: Configure TIMER which turns on LED
Interrupt Handler
6
void EXTI0_1_IRQHandler(void)
{
if ((EXTI->PR & 0x0001) != 0) /* Check line 0 has triggered the IT */
{
EXTI->PR |= 0x0001; /* Clear the pending bit */
GPIOC->ODR ^= (1<<9); /* Toggle green led on PC9 */
}
}

## Slide 32: ADC lab 7

## Slide 33: Configure ADC with continuous conv.
Objective
  Learn how to setup the ADC for continuous conversion for 4 channels
    ADC on PA1, PB1, PC0 and VREFINT
Goal
  Configure GPIO and EXTI pin
  Check the interrupt vector handler
  Show the values from ADC in the ADC_array
  GPIOA pin 0 is the EXTI pin to enable / disable the ADC
  GPIOC pin 9 is the LED used for OK
  GPIOC pin 8 is the LED used for ON / OFF conversion indication
7

## Slide 34: Configure ADC with continuous conv.
Simple code for main function and there is no loop
  Configure the GPIO
  Configure the EXTI
  Set Clock for the ADC
  Configure the ADC pins
  Enable the ADC
  Configure the ADC
  Select the first channel
  Start the conversion
7

## Slide 35: Configure ADC with continuous conv.
main function
7
ConfigureGPIO();
ConfigureExternalIT();
SetClockForADC();
CalibrateADC();
ConfigureGPIOforADC();
EnableADC();
ConfigureADC();
CurrentChannel = 0; /* Initializes the CurrentChannel */
ADC1->CR |= ADC_CR_ADSTART; /* start the ADC conversions */
while (error == 0) /* loop till no unrecoverable error, should never be exited */
{
__WFI();
}
DisableADC();
SysTick_Config(48000); /* 1ms config */
while (1); /* Infinite loop */

## Slide 36: Configure ADC with continuous conv.
Configure the GPIO used in the ADC
7
__INLINE void ConfigureGPIOforADC(void)
{
/* (1) Enable the peripheral clock of GPIOA, GPIOB and GPIOC */
/* (2) Select analog mode for PA1 */
/* (3) Select analog mode for PB1 */
/* (4) Select analog mode for PC0 */
RCC->AHBENR |= RCC_AHBENR_GPIOAEN | RCC_AHBENR_GPIOBEN | RCC_AHBENR_GPIOCEN; /* (1) */
GPIOA->MODER |= GPIO_MODER_MODER1; /* (2) */
GPIOB->MODER |= GPIO_MODER_MODER1; /* (3) */
GPIOC->MODER |= GPIO_MODER_MODER0; /* (4) */
}

## Slide 37: Configure ADC with continuous conv.
Configure ADC clock
7
__INLINE void SetClockForADC(void)
{
/* (1) Enable the peripheral clock of the ADC */
/* (2) Start HSI14 RC oscillator */
/* (3) Wait HSI14 is ready */
RCC->APB2ENR |= RCC_APB2ENR_ADC1EN; /* (1) */
RCC->CR2 |= RCC_CR2_HSI14ON; /* (2) */
while ((RCC->CR2 & RCC_CR2_HSI14RDY) == 0) /* (3) */
{
/* For robust implementation, add here time-out management */
}
}

## Slide 38: Configure ADC with continuous conv.
Configure the ADC
7
__INLINE void ConfigureADC(void)
{
/* (1) Select HSI14 by writing 00 in CKMODE (reset value) */
/* (2) Select the continuous mode and scanning direction */
/* (3) Select CHSEL1, CHSEL9, CHSEL10 and CHSEL17 */
/* (4) Select a sampling mode of 111 i.e. 239.5 ADC clk to be greater than 17.1us */
/* (5) Enable interrupts on EOC, EOSEQ and overrrun */
/* (6) Wake-up the VREFINT (only for VBAT, Temp sensor and VRefInt) */
//ADC1->CFGR2 &= ~ADC_CFGR2_CKMODE; /* (1) */
ADC1->CFGR1 |= ADC_CFGR1_CONT | ADC_CFGR1_SCANDIR; /* (2) */
ADC1->CHSELR = ADC_CHSELR_CHSEL1 | ADC_CHSELR_CHSEL9 \
| ADC_CHSELR_CHSEL10 | ADC_CHSELR_CHSEL17; /* (3) */
ADC1->SMPR |= ADC_SMPR_SMP_0 | ADC_SMPR_SMP_1 | ADC_SMPR_SMP_2; /* (4) */
ADC1->IER = ADC_IER_EOCIE | ADC_IER_EOSEQIE | ADC_IER_OVRIE; /* (5) */
ADC->CCR |= ADC_CCR_VREFEN; /* (6) */
/* Configure NVIC for ADC */
/* (7) Enable Interrupt on ADC */
/* (8) Set priority for ADC */
NVIC_EnableIRQ(ADC1_COMP_IRQn); /* (7) */
NVIC_SetPriority(ADC1_COMP_IRQn,0); /* (8) */
}

## Slide 39: Configure ADC with continuous conv.
Interrupt Handler
7
void ADC1_COMP_IRQHandler(void)
{
if ((ADC1->ISR & ADC_ISR_EOC) != 0) /* checks EOC has triggered the IT */
{
ADC_array[CurrentChannel] = ADC1->DR; /* reads data and clears EOC flag */
CurrentChannel++; /* increments the index on ADC_array */
}
if ((ADC1->ISR & ADC_ISR_EOSEQ) != 0) /* checks EOSEQ has triggered the IT */
{
ADC1->ISR |= ADC_ISR_EOSEQ; /* clears the pending bit */
CurrentChannel = 0; /* reinitialize the CurrentChannel */
GPIOC->ODR ^= (1<<9);//toggle green led on PC9
}
}

## Slide 40: Configure ADC with continuous conv.
Configure the IDE to enable the “live watch”
7

## Slide 41: UART lab 8

## Slide 42: Configure USART in loopback mode
Objective
  Learn how to setup the USART
Goal
  Configure UART TX as polling
  Configure UART RX as interrupt
  Configure LEDs and GPIO
  Connect the PA9 to the PA10 for loopbackmode
8

## Slide 43: Configure USART in loopback mode
Simple code for main function and there is no loop
  Configure the GPIO
  Configure the EXTI
  Configure the USART and USART pins
  Elable USART interrupt
8
Configure_GPIO_LED();
Configure_GPIO_USART1();
Configure_USART1();
Configure_GPIO_Button();
Configure_EXTI();
/* Reception done in USART1 IRQ handler */
/* Infinite loop */
while (1)
{
}

## Slide 44: Configure USART in loopback mode
Configure the GPIO used in USART
8
__INLINE void Configure_GPIO_USART1(void)
{
/* Enable the peripheral clock of GPIOA */
RCC->AHBENR |= RCC_AHBENR_GPIOAEN;
/* GPIO configuration for USART1 signals */
/* (1) Select AF mode (10) on PA9 and PA10 */
/* (2) AF1 for USART1 signals */
GPIOA->MODER = (GPIOA->MODER & ~(GPIO_MODER_MODER9|GPIO_MODER_MODER10))\
| (GPIO_MODER_MODER9_1 | GPIO_MODER_MODER10_1); /* (1) */
GPIOA->AFR[1] = (GPIOA->AFR[1] &~ (GPIO_AFRH_AFRH1 | GPIO_AFRH_AFRH2))\
| (1 << (1 * 4)) | (1 << (2 * 4)); /* (2) */
}

## Slide 45: Configure USART in loopback mode
Configure the USART1
8
__INLINE void Configure_USART1(void)
{
/* Enable the peripheral clock USART1 */
RCC->APB2ENR |= RCC_APB2ENR_USART1EN;
/* Configure USART1 */
/* (1) oversampling by 16, 9600 baud */
/* (2) 8 data bit, 1 start bit, 1 stop bit, no parity, tranmittion and reception mode */
USART1->BRR = 480000 / 96; /* (1) */
USART1->CR1 = USART_CR1_RXNEIE | USART_CR1_RE | USART_CR1_TE| USART_CR1_UE; /* (2) */
/* polling idle frame Transmission */
while((USART1->ISR & USART_ISR_TC) != USART_ISR_TC)
{
/* add time out here for a robust application */
}
USART1->ICR |= USART_ICR_TCCF;/* clear TC flag */
/* Configure IT */
/* (3) Set priority for USART1_IRQn */
/* (4) Enable USART1_IRQn */
NVIC_SetPriority(USART1_IRQn, 0); /* (3) */
NVIC_EnableIRQ(USART1_IRQn); /* (4) */
}

## Slide 46: Configure USART in loopback mode
Interrupt Handler for the Button pressed
8
void EXTI0_1_IRQHandler(void)
{
EXTI->PR |= 1;
/* start USART transmission */
USART1->TDR = stringtosend[send++]; /* Will inititiate TC if TXE */
if(send > 1)
{
send = 0;
}
}

## Slide 47: Configure USART in loopback mode
Interrupt Handler for the USART Reception
8
void USART1_IRQHandler(void)
{
uint8_t chartoreceive = 0;
if((USART1->ISR & USART_ISR_RXNE) == USART_ISR_RXNE)
{
chartoreceive = (uint8_t)(USART1->RDR); /* Receive data, clear flag */
switch(chartoreceive)
{
case 'G': GPIOC->ODR ^= GPIO_ODR_9; /* toggle green LED */
break;
case 'O': GPIOC->ODR ^= GPIO_ODR_8; /* toggle orange LED */
break;
default: break;
}
}
}

## Slide 48: Thank You